## Slide 1
Chapter 11: Network Address Translation for IPv4
Cisco Confidential
Routing & Switching

## Slide 2: Chapter 11
Cisco Confidential
  NAT Operation
  Configuring NAT
  Troubleshooting NAT
  Summary

## Slide 3: Chapter 11: Objectives
Cisco Confidential
Describe NAT characteristics.
Describe the benefits and drawbacks of NAT.
Configure static NAT using the CLI.
Configure dynamic NAT using the CLI.
Configure PAT using the CLI.
Configure port forwarding using the CLI.
Configure NAT64.
Use show commands to verify NAT operation.

## Slide 4: 11.1 NAT Operation
Cisco Confidential

## Slide 5: IPv4 Private Address Space
NAT Characteristics
Cisco Confidential
IPv4 address space is not big enough to uniquely address all the devices that must be connected to the Internet.
Network private addresses are described in RFC 1918 and are to
designed to be used within an organization or site only.
Private addresses are not routed by Internet routers while public addresses are.
Private addresses can alleviate IPv4 scarcity, but because they aren’t
routed by Internet devices, they first need to be translated.
NAT is process used to perform such translation.

## Slide 6: IPv4 Private Address Space
NAT Characteristics
Cisco Confidential

## Slide 7: What is NAT?
NAT Characteristics
Cisco Confidential
NAT is a process used to translate network addresses.
NAT’s primary use is to conserve public IPv4 addresses.
NAT is usually implemented at border network devices, such as
firewalls or routers.
NAT allows the networks to use private addresses internally, only translating to public addresses when needed.
Devices within the organization can be assigned private addresses
and operate with locally unique addresses.
When traffic must be sent or received to or from other organizations or the Internet, the border router translates the addresses to a public and globally unique address.

## Slide 8: What is NAT? (cont.)
NAT Characteristics
Cisco Confidential

## Slide 9: NAT Terminology
NAT Characteristics
Cisco Confidential
Inside network is the set of devices using private addresses
Outside network refers to all
other networks
NAT includes four types of addresses:
  Inside local address
  Inside global address
  Outside local address
  Outside global address

## Slide 10: NAT Terminology (cont.)
NAT Characteristics
Cisco Confidential

## Slide 11: Static NAT
Types of NAT
Cisco Confidential
Static NAT uses a one-to-one mapping of local and global addresses.
These mappings are configured by the network administrator and remain constant.
Static NAT is particularly useful when servers hosted in the inside
network must be accessible from the outside network.
A network administrator can SSH to a server in the inside network by pointing the SSH client to the proper inside global address.

## Slide 12: Static NAT (cont.)
Types of NAT
Cisco Confidential

## Slide 13: Dynamic NAT
Types of NAT
Cisco Confidential
Dynamic NAT uses a pool of public addresses and assigns them on a first-come, first-served basis.
When an inside device requests access to an outside network, dynamic NAT assigns an available public IPv4 address from the pool.
Dynamic NAT requires that enough public addresses are available to satisfy the total number of simultaneous user sessions.

## Slide 14: Dynamic NAT (cont.)
Types of NAT
Cisco Confidential

## Slide 15: Port Address Translation
Types of NAT
Cisco Confidential
Port Address Translation (PAT) maps multiple private IPv4 addresses to a single public IPv4 address or a few addresses.
PAT uses the pair source port and source IP address to keep track
of what traffic belongs to what internal client.
PAT is also known as NAT overload.
By also using the port number, PAT forwards the response packets to the correct internal device.
The PAT process also validates that the incoming packets were
requested, thus adding a degree of security to the session.

## Slide 16: Comparing NAT and PAT
Types of NAT
Cisco Confidential
NAT translates IPv4 addresses on a 1:1 basis between private IPv4
addresses and public IPv4 addresses.
PAT modifies both the address and the port number.
NAT forwards incoming packets to their inside destination by referring to the incoming source IPv4 address provided by the host on the public network.
With PAT, there is generally only one or a very few publicly exposed IPv4 addresses.
PAT is able to translate protocols that do not use port numbers, such as ICMP; each one of these protocols is supported differently by PAT.

## Slide 17: Benefits of NAT
Benefits of NAT
Cisco Confidential
Conserves the legally registered addressing scheme
Increases the flexibility of connections to the public network
Provides consistency for internal network addressing schemes
Provides network security

## Slide 18: Disadvantages of NAT
Benefits of NAT
Cisco Confidential
Performance is degraded
End-to-end functionality is degraded
End-to-end IP traceability is lost
Tunneling is more complicated
Initiating TCP connections can be disrupted

## Slide 19: 11.2 Configuring NAT
Cisco Confidential

## Slide 20: Configuring Static NAT
Configuring Static NAT
Cisco Confidential
There are two basic tasks to perform when configuring static NAT translations:
Create the mapping between the inside local and outside local addresses.
Define which interfaces belong to the inside network and which belong to the outside network.

## Slide 21: Configuring Static NAT
Configuring Static NAT
Cisco Confidential

## Slide 22: Analyzing Static NAT
Configuring Static NAT
Cisco Confidential

## Slide 23: Verifying Static NAT
Configuring Static NAT
Cisco Confidential

## Slide 24: Verifying Static NAT (cont.)
Configuring Static NAT
Cisco Confidential

## Slide 25: Dynamic NAT Operation
Configuring Dynamic NAT
Cisco Confidential
The pool of public IPv4 addresses (inside global address pool) is available to any device on the inside network on a first-come, first- served basis.
With dynamic NAT, a single inside address is translated to a single
outside address.
The pool must be large enough to accommodate all inside devices.
A device is unable to communicate to any external networks if no
addresses are available in the pool.

## Slide 26: Configuring Dynamic NAT
Configuring Dynamic NAT
Cisco Confidential

## Slide 27: Analyzing Dynamic NAT
Configuring Dynamic NAT
Cisco Confidential

## Slide 28: Analyzing Dynamic NAT
Configuring Dynamic NAT
Cisco Confidential

## Slide 29: Verifying Dynamic NAT
Configuring Dynamic NAT
Cisco Confidential

## Slide 30: Verifying Dynamic NAT
Configuring Dynamic NAT
Cisco Confidential

## Slide 31: Configuring PAT: Address Pool
Configuring PAT
© 2008 Cisco Systems, Inc. All rights reserved. Cisco Confidential
31

## Slide 32: Configuring PAT: Single Address
Configuring PAT
48
Cisco Confidential

## Slide 33: Analyzing PAT
Configuring PAT
48
Cisco Confidential

## Slide 34: Analyzing PAT
Configuring PAT
48
Cisco Confidential

## Slide 35: Verifying PAT Translations
Configuring PAT
48
Cisco Confidential

## Slide 36: Port Forwarding
Port Forwarding
48
Cisco Confidential
Port forwarding is the act of forwarding a network port from one
network node to another.
A packet sent to the public IP address and port of a router can be forwarded to a private IP address and port in inside network.
Port forwarding is helpful in situations where servers have private
addresses, not reachable from the outside networks.

## Slide 37: SOHO Example
Port Forwarding
48
Cisco Confidential

## Slide 38: Configuring Port Forwarding with IOS
Port Forwarding
In IOS, Port forwarding is essentially a static NAT translation with a specified TCP or UDP port number.
48
Cisco Confidential

## Slide 39: NAT for IPv6?
Configuring NAT and IPv6
48
Cisco Confidential
NAT is a workaround for IPv4 address scarcity.
IPv6 with a 128-bit address provides 340 undecillion addresses.
Address space is not an issue for IPv6.
IPv6 makes IPv4 public-private NAT unnecessary by design; however, IPv6 does implement a form of private addresses, and it is implemented differently than they are for IPv4.

## Slide 40: IPv6 Unique Local Addresses
Configuring NAT and IPv6
IPv6 unique local addresses (ULAs) are designed to allow IPv6 communications within a local site.
ULAs are not meant to provide additional IPv6 address space.
ULAs have the prefix FC00::/7, which results in a first hextet range
of FC00 to FDFF.
ULAs are also known as local IPv6 addresses (not to be confused with IPv6 link-local addresses).
48
Cisco Confidential

## Slide 41: NAT for IPv6
Configuring NAT and IPv6
48
Cisco Confidential
IPv6 also uses NAT, but in a much different context.
In IPv6, NAT is used to provide transparent communication between IPv6 and IPv4.
NAT64 is not intended to be a permanent solution; it is meant to be a transition mechanism.
Network Address Translation-Protocol Translation (NAT-PT) was another NAT-based transition mechanism for IPv6, but is now deprecated by IETF.
NAT64 is now recommended.

## Slide 42: NAT for IPv6
Configuring NAT and IPv6
48
Cisco Confidential

## Slide 43: 11.3 Troubleshooting NAT
48
Cisco Confidential

## Slide 44: Troubleshooting NAT: show commands
Configuring NAT and IPv6
48
Cisco Confidential

## Slide 45: Troubleshooting NAT: debug command
Configuring NAT and IPv6
48
Cisco Confidential

## Slide 46: Chapter 11: Summary
48
Cisco Confidential
This chapter has outlined:
How NAT is used to help alleviate the depletion of the IPv4 address space.
NAT conserves public address space and saves considerable administrative overhead in managing adds, moves, and changes.
NAT for IPv4, including:
  NAT characteristics, terminology, and general operations
  Different types of NAT, including static NAT, dynamic NAT, and
NAT with overloading
  Benefits and disadvantages of NAT
The configuration, verification, and analysis of static NAT, dynamic NAT, and NAT with overloading.

## Slide 47: Chapter 11: Summary (cont.)
48
Cisco Confidential
How port forwarding can be used to access an internal devices from
the Internet.
Troubleshooting NAT using show and debug commands.
How NAT for IPv6 is used to translate between IPv6 addresses and IPv4 addresses.

## Slide 48
48
Cisco Confidential